## Slide 1
A new biped: CornellX MkIII
More stats Stairs, squats Up to 200 Nm joint torque 0.2 s leg swing Up to 15 rad/sec joint speed
1.5 m tall 0.8 m legs
Open source design
Jason Cortell, Peter Baggaley, and Andy Ruina
Cornell Ranger, 65 km
CornellX MkIII
Agile and Efficient
Robust balance
Fast foot placement
More speed, more torque
Robot | Motors | Mass | Peak joint power | CoT
Ranger | 3 | 10 kg | 100 W => 10 W/kg | 0.2
CornellX MkIII | 12 | 30 kg | 3000 W => 100 W/kg | 0.25
Fast foot placement AND low CoT
Fine-tuned motors, controllers, and transmissions
Low leg and motor rotor inertia
Robust
Capable
3D
and efficient too

## Slide 2
Chains and sprockets + high power/weight, efficient, flexible - not modular, backlash, + cheap custom parts - bulky (36 chains & 72 sprockets)
Biarticular ankle and knee Low leg inertia
Collision tolerance Motor backs off at impact Low-inertia motor Series compliance Overload clutches
CornellX MkIII
Electronics
Sensing and computing < 7 W
Custom motor controllers
2 angle sensors per DoF (motor + joint)
1 Atmel ARM MCU per motor
BeagleBone Black main brain, 1 GHz ARM
Drive mechanisms uncovered